## Slide 1
Woodchipper Design
Machine Elements 2 | Market Research, Calculation & Design Plan
Nipun Gunarathne
Antony Akwalu
Levente Cseszkó
Gaurawa Kovida

## Slide 2
Project Scope & Objectives
To design, calculate, and document a complete, safe, and mobile woodchipper based on the provided 7.5 kW motor specification.

## Slide 3
Cutter & Housing
Design a disc cutter, main shaft, and protective housing. Target 50mm branch capacity.
Drivetrain Calculation
Calculate and document the full power transmission: belt drive, shaft loads, and bearing selection.
Frame & Mobility
Create a stable sheet metal frame on a mobile platform for transport and operation.
Safety & Function
The final design must be functional, with all guards and safety features included.
Core Project Requirements

## Slide 4
Market Research
Analyzing the "Prosumer" (7.5 kW) woodchipper market to establish our design philosophy.

## Slide 5
1. High-Speed / Low-Torque (Budget)
These are often direct-driven from 3600 RPM petrol engines, spinning the cutter at 2200-3000+ RPM.
Pros: Cheap to build (no reduction), lighter flywheel.
Cons: Lower torque (stalls on 50mm+ wood), high noise, and faster wear on knives and bearings.
2. Moderate-Speed / High-Torque (Premium)
Uses a deliberate belt reduction from a high-speed motor to run the cutter at 1300-2000 RPM.
Pros: Vastly superior torque, ideal for a heavy flywheel, powers through tough wood, and longer component life.
Cons: Requires a heavier disc and a calculated drive system.
Market Analysis: Competing Designs

## Slide 6
2x
More Torque
Why 1460 RPM is the Smart Choice
The law of power is P = T · ω (Power = Torque × Speed).
By using a 2:1 belt reduction (2920 RPM → 1460 RPM), we halve the speed but double the available torque at the cutter disc. This high torque, combined with a heavy flywheel, allows our 7.5 kW motor to easily chip 50mm branches without stalling.
Our Philosophy: Engineer for Torque

## Slide 7
Design Justification

## Slide 8
Drivetrain Design & Calculation
Translating our philosophy into a calculated, engineered system. (Ref: Optibelt Technical Manual)

## Slide 9
Step 1: Design Power (PB) & Belt Profile
A Service Factor of 1.6 is selected for a heavy-duty, 16+ hour operation with shock loads (per Optibelt Table 23).
Requirement: 7.5 kW Electric motor
As per the Optibelt catalogue, SPZ V belts are used.
(Design power 7.5*1.6= 12 kW)

## Slide 10
Parameter | Symbol | Value | Notes
Motor Speed (n₁) | n1 | 2920 RPM | From SEVA-tec motor specs.
Target Cutter Speed (n₂) | n2 | 1460 RPM | Project requirement.
Target Gear Ratio | i | 2.0 | -
Small Pulley (Motor) | ddk | 106 mm | Standard SPZ Taper-Lock size.
Large Pulley (Cutter) | ddg | 212 mm | Standard SPZ Taper-Lock size.
Std. Belt Length | Ldst | 1500 mm | Selected for standard center distance= 497.6 mm (in range).
Step 2: Pulleys, Belt Length & Ratios

## Slide 11
Parameter | Symbol | Value | Notes
Belt Speed | v | 16.2 m/s | PASSED. (Limit: 42 m/s for SPZ)
Flex Rate | fb | 21.6 Hz | PASSED. (Limit: 100 Hz)
Nominal Power / Belt | PN | 4.8 kW | Optibelt Table 41 (SPZ, 106mm, 2920rpm)
Correction Factors | c1,c3 | 0.99 | From the catalogue
Calculated Belts | z | 2.57 | -
Final Selection | zdst | 3 Belts | Always round up. (SPZ 1500)
Step 3: Number of Belts (z) & Sanity Checks

## Slide 12
Parameter | Symbol | Value | Notes
Design Requirement | Vc | > 25 m/s | Minimum tip speed for effective chip ejection (Ref: Reczulski, 2015).
Min. Diameter | Dmin | 327 mm | Using the given equations.
Selected Diameter | Ddst | 400 mm | Selected for higher inertia (flywheel effect).
Final Tip Speed | Vc | 30.58 m/s | PASSED.
Step 4: Cutter Disc Sizing (Tip Speed)

## Slide 13
Parameter | Symbol | Value | Notes
Max. Shaft Load (from Step 3) | Smax | 1158 N | This is the peak bending force F from the belts.
Torsional Moment (Torque) | Mt | 49.2 Nm | -
Assumed Overhang | a | 60 mm | Assumed distance from bearing to pulley center.
Bending Moment | Mb | 69.5 Nm | -
Equivalent Torque | Te | 85.15 Nm | Combines both loads.
Step 5: Shaft Load Analysis (Moments)

## Slide 14
Parameter | Symbol | Value | Notes
Material | - | C45 Steel | Good strength and machinability.
Shear Yield Strength | ty | ~170 MPa | -
Factor of Safety | n | 4.0 | High value chosen for shock/impact loads.
Allowable Shear Stress | tallow | 42.5 MPa | -
Min. Required Diameter | dmin | 21.7 mm | -
Final Selected Diameter | d | 35 mm | Standard size, accounts for keyway & shock.
Step 6: Shaft Diameter Calculation (d)

## Slide 15
Parameter | Symbol | Value | Notes
Standard Key (DIN 6885) | b*h | 10mm x 8mm | For a 35mm shaft.
Allowable Pressure | pallow | 60 MPa | Conservative value for shock loads.
Shaft Keyway Depth | t1 | 5 mm | Standard for 8mm high key.
Min. Length (Pressure) | lp | 15.87 mm | -
Min. Length (Shear) | lt | 4.76 mm | Shear is not the limiting factor.
Final Key Selection | - | 10x8x25 mm | 25mm is a standard length > 15.87mm.
Step 7: Keyway Sizing (for 35mm Shaft)

## Slide 16
Component | Parameter | Final Selected Value
Motor | Power / Speed | 7.5 kW / 2920 RPM
Cutter Disc | Diameter / Speed | 400 mm / 1460 RPM
Belt Drive | Type / Quantity | 3 x SPZ 1500 V-Belts
Pulleys | Motor / Cutter | 106 mm / 212 mm (SPZ)
Shaft | Material / Diameter | C45 Steel / 35 mm
Key | Type (Cutter) | 10mm x 8mm x 25mm (Parallel Key)
Loads for CAD | Max. Shaft Load (Sa) | 1158 N (Bending)
Loads for CAD | Max. Shaft Torque (Mt) | 49.2 Nm (Torsion)
Calculation Summary: Final Design Values

## Slide 17
Our design competes with premium machines (€3,000 - €5,000).
By manufacturing the chassis/cutter in-house, our component cost will be a fraction of this retail price.
Rough Cost Analysis

## Slide 18
Phase 1: Detailed CAD Modeling Model the 400mm cutter disc, 35mm main shaft, and sheet metal frame.
Phase 2: Component Sourcing Download 3D models for the SEVA-tec motor, standard taper-lock pulleys (SPZ 106/212), and bearings (for 35mm shaft).
Phase 3: Analysis & Assembly Run shaft analysis (FEA) using the 1158 N bending load and 49.2 Nm torque. Confirm bearing selection.
Phase 4: Safety & Finalization Model all safety guards (belt guard, infeed/outfeed hoppers) and create final manufacturing drawings and report.
Project Plan: Future Work

## Slide 19
Thank you for your attention.